## Slide 1: CLUB AUTOMATION
A Sci-Tech Summer Camp Project
ROBOTICS CLUB, IIT KANPUR
presents

## Slide 2: What the project is about…..
--To automate various parts of Robotics Club Room, like lights, fans, switches etc., and develop a user interface and web server for use.
--Various modules of the project include:
Android app for user control
Web Server for remote access
Raspberry Pi as the control unit
Relays with Arduino to trigger electrical circuit

## Slide 3
App sends request to server ⇒ Database in server gets updated ⇒ Server sends response to R-pi ⇒ R-pi runs Arduino ⇒ Arduino controls the Relays ⇒ Relay acts as switch for the electrical circuit
PROJECT OUTLINE
Web
Server
Android App
R-Pi
Arduino
Relay Channel
Various Room Appliances

## Slide 4
Developed an android app which can send an HTTP request to our webserver and display the response.
Development in form of a list view consisting of toggle buttons for the appliances.
Achieved this using the Volley Library, an HTTP library that made networking faster.
The benefits offered are:
  Automatic scheduling of network requests.
  Cancellation request API - can cancel a single request, or can set blocks or scopes of requests to cancel.
  Ease of customization, for example, for retry.
Android App Development

## Slide 5
GUI (Graphic User Interface) of our app
The Login Page
The Sign Up Page
The Control Page
Not included in the current project

## Slide 6
The Raspberry Pi is a small single board complete Linux computer. We use it as a control system
A web server is a computer system that processes requests via HTTP.
We have:
>Successfully created a local database and server. The database gets updated when a request is sent to the server through the R-Pi which is operated through terminal by installing Raspbian OS.
WEB server and r-pi


## Slide 7
Initially the state of Fan was
1 == ‘ON’
Server gets a request from the user to turn off Fan1
The state of Fan1 changes from
1 to 0 in the database i.e. now
the fan is turned off
Working of Server

## Slide 8
Arduino is an open source single-board microcontrollers for building digital devices and interactive objects that can sense and control objects in the physical world.
A relay is an electrically operated switch, which when connected to OS like Arduino or At-Mega, can be used to automate electric circuits which switch on and off on simple binary commands through connected web server.
Relay module and Arduino

## Slide 9
Using an operating system, we program the Arduino to control the relay. The lights and fans are connected to the relay and thus can be switched on/off on command of a single button.

## Slide 10
PROJECT DEMO VIDEO
Please Click the Link to see the demo video of the project.
If all queries are satisfied, we can take the project to the next level and connect the actual appliances in the club room.
LINK TO VIDEO

## Slide 11
Door Lock
Temperature Monitor
People Counter
Motion Detection
Curtains Control
Fire Alarm
CLUB
AUTOMATION
Future Aspects
Of
The project
Security System and Surveillance
Controlling Fan Speed

## Slide 12
TEAM MEMBERS
R-pi & Web Server
Relay Circuit & Arduino
Android App
Subham Kumar Garvit Airen Shruti Shukla
Rahul Chauhan Sagar Chaudhary
Jeevan Kumar
Mentors: Amit Saharan Saurabh Ranjan Akash Gupta Akash Jain Ujjwal Varshney

## Slide 13
Any Questions?

## Slide 14
Thank You
The End